NG TF V8 B9BOC SPECIFICATION

CHASSIS

Standard NG ladder chassis, powder coated and Waxoyle filled.

BODY

GRP tub and wings, gel coated red.

Aluminium louvred bonnet.

Professionally sprayed red with lacquer coat.

Folding windscreen

Aero screens

2 spot/driving lights

Luggage rack

ENGINE

Rebuilt Rover V8 3.9l, Stage 1 tuned, Piper fast road camshaft, lightened and balanced flywheel and clutch.

ENGINE COOLING

Thermostatically controlled electric radiator fan.

Thermostatically controlled oil cooler.

CARBURETTOR

Weber 4 barrel downdraft on Edelbrock Performer manifold, pancake air filter.

IGNITION

Mallory Unilite electronic ignition system, high performance coil with ballast resistor.

TRANSMISSION

New clutch and bell housing.

New R380 5 speed gear box.

High torque prop shaft.

Cosworth limited slip differential.

SUSPENSION

Hoyle Engineering double wishbone independent suspension front and rear.

Adjustable coil-over dampers.

BRAKES

Disk brakes front and rear with ventilated disks and four pot calipers on front.

Dual circuit.

STEERING

MGB rack and pinion.  Motolita collapsible steering wheel.

INTERIOR

Walnut veneer dash, fully instrumented.

Ivory leather covered seats, trim and steering wheel, fully carpeted interior (dark red).

Heater.

WHEELS

5 MGC 72-spoke 15 inch chrome/stainless wire wheels with knock-off hubs.  Pirelli P3000 tyres with inner tubes.  Spare unused.

ELECTRICS

Designed and built for maximum reliability and serviceability.  Alarm/demobiliser incorporated into the wiring. 8 relays, 16 fuses plus 100amp master Megafuse. All heavy current items switched via relays.  Separate fuses for main, dip, left and right side lights. All 12v return lines are taken to only two earthing points. High capacity battery. Wire colours comply with industry standards. Full set of wiring diagrams, relay and fuse details and wire lists supplied.

PROTECTION

Side screens

Beige mohair hood

Beige mohair split tonneau cover

Fitted rain cover

Fitted dust cover